## Slide 1: Spectre (CVE-2017-5753)
By Jose Ramirez

## Slide 2: When was it found?
The vulnerability was found on June 1, 2017.
According to The Verge, the first to find the vulnerability was Jann Horn, from Google Project Zero.
Another team from Graz university of Technology alerted Intel about the vulnerability on December 3rd 2017
Publicly disclosed on January 3rd, 2018

## Slide 3: The Basics: Speculative Execution
3
The vulnerability involves speculative references and execution.
CPU’s use speculative execution and references to predict outcomes before they are properly determined.
The CPU will create a checkpoint of its current register state and execute its prediction.
When the CPU checks the proper outcome, it will either:
  Be wrong and revert back to the checkpoint, then execute the right outcome.
  Be right and continue with execution,.

## Slide 4: The Vulnerability: Transient Instructions
Spectre attacks take advantage of speculative execution by using transient instructions.
Transient instructions are instruction sequences, that should not have been executed, being executed by the CPU through speculative execution.
Since they are not the correct executions, the CPU will revert to its checkpoint state and move onto the correct execution, but it does not revert the cached memory.
Spectre attacks will influence the transient instructions and allow the attacker to obtain leaked information from the victims memory address space (cached memory).

## Slide 5
5
  Variant 1: Exploiting Conditional Branches
    The Spectre attack first mistrains the CPU’s branch predictor into mispredicting branch execution.
    This can then be used to temporarily execute code.
    This allows the attacker to read information from the programs cached space. (Information Exposure)
The Attacks: Exploiting Conditional and Indirect Branches
  Variant 2: Exploiting Indirect Branches
    This attack trains the CPU’s branch target buffer into indirectly reaching to an application/programs memory address.
    This causes the application/program to execute and its information is cached.
    The CPU realizes it is not the intended result and reverts back to its previous checkpoint, but the cached information created can be read by the attacker.

## Slide 6: The Remedy: Patch and Pray
6
All of the vendors affected released patches for Spectre and Meltdown.
Microsoft even released a PowerShell script that tests to make sure you are not vulnerable to Spectre.
Sadly, there are more variants of Spectre like attacks being found, one of the latest being SWAPGS. SWAPGS is a variant of Specter variant 1.
It was disclosed on August 6, 2019
Although it has already been patched, who knows how many more variants are being used that have not been discovered.

## Slide 7
7
  Variant 1: Exploiting Conditional Branches
    The Spectre attack first mistrains the CPU’s branch predictor into mispredicting branch execution.
    This can then be used to temporarily execute code.
    This allows the attacker to read information from the programs cached space. (Information Exposure)
References
Brandom, R. (2018, January 11). How an industry-breaking bug stayed secret for seven months. Retrieved from https://www.theverge.com/2018/1/11/16878670/meltdown-spectre-disclosure-embargo-google-microsoft-linux
Computer Hope. (2018). What is a Speculative Execution?. Retrieved from https://www.computerhope.com/jargon/s/spec-exec.htm
Computer Hope. (2018). speculating-cpu [model]. Retrieved from https://www.computerhope.com/jargon/s/speculating-cpu.jpg
Larabel, M. (2019, August 6). CVE-2019-1125 "SWAPGS" Is The Newest Spectre Vulnerability. Retrieved from https://www.phoronix.com/scan.php?page=news_item&px=CVE-2019-1125-SWAPGS
Liska, A. (2018, January 4). Vendors Rush to Patch Meltdown and Spectre Vulnerabilities. Retrieved from https://www.recordedfuture.com/meltdown-spectre-vulnerabilities/
Liska, A. (2018, January 4). meltdown-spectre-vulnerabilities [Model]. Retrieved from https://www.recordedfuture.com/wp-content/uploads/meltdown-spectre-vulnerabilities.png
Miessler, D. (2018). Meltdown-and-Spectre-Severe-CPU-vulnerabilities [comparison table]. Retrieved from https://www.blackmoreops.com/wp-content/uploads/2018/01/Meltdown-and-Spectre-Severe-CPU-vulnerabilities.png
NVD. (2018, January 4). CVE-2017-5753. Retrieved from https://nvd.nist.gov/vuln/detail/CVE-2017-5753#
Yarom, Y., Shwarz, M., Hamburg, M., Lipp, M., Kocher, P., Haas, W., … Genkin, D. (2018, January 4). Spectre Information Disclosure Proof Of Concept ≈ Packet Storm. Retrieved from https://packetstormsecurity.com/files/145645/Spectre-Information-Disclosure-Proof-Of-Concept.html